## Slide 1
Assembly Language Syntax
ARM assembler commonly uses following instruction format:
label opcode operand1, operand2, operand3, … ; Comment
Label is an optional first field of an assembly statement.
Labels are alphanumeric names used to define the starting location of a block of statements.
When creating the executable file the assembler will replace the label with the assigned value.
Labels must be unique in the executable file because an identical label encountered by the Assembler will generate an error.
ARM assembler has reserved first character of a line for the label field and it should be left blank for the instructions with no labels.

## Slide 2
Assembly Language Syntax
Opcode is the second field in assembly language instruction.
Assembly language consists of mnemonics, each corresponding to a machine instruction.
Using a mnemonic you can decide what operation you want to perform on the operands.
Assembler must translate each mnemonic opcode into their binary equivalent.
Next to the opcode is the operand field which might contain different number of operands.
Some of the instructions in Cortex-M3 will have no operand while other might have as many as four operands.
The number of operands in an instruction depends on the type of instruction, and the syntax format of the operand can also be different.
Normally, the first operand is the destination of the operation.

## Slide 3
Assembly Language Syntax
Comments are messages intended only for human consumption.
They have no effect on the translation process and indeed are not acted on by the ARM Assembler.
The comment field of an assembly language instruction is also optional.
A semicolon signifies that the rest of the line is a comment and is to be ignored by the assembler.
If the semicolon is the first non-blank character on the line, the entire line is ignored.
If the semicolon follows the operands of an instruction, then only the comment is ignored by the assembler.

## Slide 4
Assembler Directives
Every program to be executed by a computer is a sequence of statements that can be read by the humans.
An assembler must differentiate between the statements that will be converted into executable code and that instruct the assembler to perform some specific function.
Assembler directives are commands to the assembler that direct the assembly process.
Assembler directives are also called pseudo opcodes or pseudo-operations.
They are executed by the assembler at assembly time not by the processor at run time.
Machine code is not generated for assembler directives as they are not directly translated to machine language.
Some tasks performed by these directives are:
1. Assign the program to certain areas in memory.
2. Define symbols.
3. Designate areas of memory for data storage.
4. Place tables or other fixed data in memory.
5. Allow references to other programs.

## Slide 5
AREA Directive
AREA directive allows the programmer to specify the memory location to store code and data.
Depending on the memory configuration of your device, code and data can reside in different areas of memory.
A name must be specified for an area directive.
There are several optional comma delimited attributes that can be used with AREA directive.

## Slide 6
ENTRY and END Directives
The first instruction to be executed within an application is marked by the ENTRY directive.
Entry point must be specified for every assembly language program.
An application can contain only a single entry point and so in a multi-source module application, only a single module will contain an ENTRY directive.
END directive causes the assembler to stop processing the current source file.
Every assembly language source module must therefore finish with this directive

## Slide 7
ALIGN Directive
Use of ALIGN ensures that your code is correctly aligned.
By default, the ALIGN directive aligns the current location within the code to a word (4-byte) boundary.
ALIGN 2 can also be used to align on a halfword (2-byte) boundary in Thumb code.
As a general rule it is safer to use ALIGN frequently through your code.
Data Reservation Directives (DCB, DCD, DCW)
ARM assembler supports different data definition directives to insert constants in assembly code.
This directive allows the programmer to enter fixed data into the program memory and treats that data as a permanent part of the program.
Different variants of these directives are:
1. DCB (Define Constant Byte) to define constants of byte size.
2. DCW (Define Constant Word) allocates one or more half words of memory, aligned on two-byte boundaries.
3. DCD (Define Constant Data) allocates one or more words of memory, aligned on four-byte boundaries.

## Slide 8
SPACE Directive
The SPACE directive reserves a zeroed block of memory.
ALIGN directive must be used to align any code following a SPACE directive.

## Slide 9
Example 1 ADDITION
AREA Example1, CODE, READONLY
ADD r0,r1,r2
ADD r0,r3
Stop B Stop
END
1. The semicolon indicates a user-supplied comment. Anything following a semicolon on the same line is ignored by the assembler.
2. The first line is AREA Example1, CODE, READONLY is an assembler directive and is required to set up the program. In this case, AREA refers to the segment of code, Example1 is the name we’ve given it, CODE indicates executable code rather than data, and READONLY state that it cannot be modified at run time.
3. Anything starting in column 1 (in this case Stop) is a label that can be used to refer to that line.
4. The instruction Stop B Stop means ‘Branch to the line labelled Stop’ and is used to create an infinite loop. This is a convenient way of ending programs in simple examples like these.
5. The last line END is an assemble directive that tells the assembler there is not more code to follow. It ends the program.

## Slide 10
Example 2 ADDITION
AREA Example2, CODE, READONLY
MOV r1,#Q ;load r1 with the constant Q
MOV r2,#R
MOV r3,#S
ADD r0,r1,r2
ADD r0,r0,r3
Stop B Stop
Q EQU 2 ;Equate the symbolic name Q to the value 2
R EQU 4 ;
S EQU 5 ;
END

## Slide 11
Example 3 ADDITION
AREA Example3, CODE, READONLY
LDR r1,Q ;load r1 with Q
LDR r2,R ;load r2 with R
LDR r3,S ;load r3 with S
ADD r0,r1,r2 ;add Q to R
ADD r0,r3 ;add in S
STR r0,Q ;store result in Q
Stop B Stop
P SPACE 4 ;save one word of storage
Q DCD 2 ;create variable Q with initial value 2
R DCD 4 ;create variable R with initial value 4
S DCD 5 ;create variable S with initial value 5
END
Q DCD 2 ;create variable Q with initial value 2, means ‘call the current line Q and store the word 0x00000002 at that location.