## Slide 1: IP Addressing

## Slide 2: What is IP address?
IP address is a 32 bit sequence of 0s and 1s
A way to identify machine on a network
A unique identifier
A numerical label

## Slide 3: IP Usage
Used to connect to another computer
Allow transfer of files or exchange of information

## Slide 4: Services provided by IP
Addressing
Fragmentation

## Slide 5: IP Terminology
Several Important terms to understand IP
BIT :- A bit is one digit; either a 1 or a 0
BYTE :- A byte is 7 or 8 bits, depending on whether parity, always assume a byte is 8 bits
OCTET:- An octet, made up of 8 bits

## Slide 6: IP Structure
IP address consist of four sections
Each section is 8bits long
Each section can range from 0 to 255
Example 192.168.1.18

## Slide 7: Parts of IP Address
Network part
Host part

## Slide 8
Network | Host | Host | Host
Network | Network | Host | Host
Network | Network | Network | Host
Class C :
Class B :
Class A :
Class D :
Class E :
Multicast
Research
8 bits | 8 bits | 8 bits | 8 bits
Parts of IP Address

## Slide 9: IP Classes
Class A
Class B
Class C
Class D
Class E

## Slide 10: Private and Public IP address
Private – A range of IP address reserved for local area network; it is free
Public – To connect or travel in internet we need public IP address; it is chargeable
*To find public ip address of your system or mobile type the following URL: https://www.ipchicken.com/

## Slide 11: Private IP Address
Address class | Reserved address space
Class A | 10.0.0.0 through 10.255.255.255
Class B | 172.16.0.0 through 172.31.255.255
Class C | 192.168.0.0 through 192.168.255.255

## Slide 12: IP Versions

## Slide 13: Allocation of IP address
Static Address (Assigning IP address manually)
Dynamic Address (Server will assign IP address automatically to hosts using DHCP / BOOTP protocols)

## Slide 14: IP Commands
Windows:
  ipconfig or ipconfig /all (to find the ip address assigned to your system)
Unix / Linux:
  Ifconfig (to find the ip address assigned to your system)

## Slide 15: Network Masks
Distinguishes which portion of the address identifies the network and which portion of the address identifies the node.
Default masks:
  Class A: 255.0.0.0
  Class B: 255.255.0.0
  Class C: 255.255.255.0

## Slide 16: Subnetting
The process of dividing a single network into multiple sub networks is called as subnetting.
The sub networks so created are called as subnets.

## Slide 17: Subnetting
Creates multiple logical networks that exist within a single Class A, B, or C network.
If you do not subnet, you will only be able to use one network from your Class A, B, or C network, which is unrealistic
Each data link on a network must have a unique network ID, with every node on that link being a member of the same network

## Slide 18: Benefits of Subnetting
Reduced network traffic
Optimized network performance
Simplified management
Facilitated spanning of large geographical distances

## Slide 19: How to create subnets
Determine the number of required network IDs:
  One for each subnet
  One for each wide area network connection
Determine the number of required host IDs per subnet:
  One for each TCP/IP host
  One for each router interface
Based on the above requirements, create the following:
  One subnet mask for your entire network
  A unique subnet ID for each physical segment
  A range of host IDs for each subnet

## Slide 20: Subnetting a Class A/B/C Address
How many subnets does the chosen subnet mask produce?
How many valid hosts per subnet are available?
What are the valid subnets?
What’s the broadcast address of each subnet?
What are the valid hosts in each subnet?

## Slide 21: Subnetting types
Fixed Length
  All the subnets are of same size.
  All the subnets have equal number of hosts.
  All the subnets have same subnet mask.
Variable Length Subnet Mask
  All the subnets are not of same size.
  All the subnets do not have equal number of hosts.
  All the subnets do not have same subnet mask.

## Slide 22: Problem - 1

## Slide 23: Fixed Length subnet masking
Consider an address block 121.37.10.64 /26.
Find the first and last addresses for each subnet, if the number of equal sized subnets required is as given in the input.
Number of subnets required = 4
Result:
Subnet-1:
First Address: 121.37.10.64 /28
Last Address: 121.37.10.79 /28
Subnet-2:
First Address: 121.37.10.80 /28
Last Address: 121.37.10.95 /28
Subnet-3:
First Address: 121.37.10.96 /28
Last Address: 121.37.10.111 /28
Subnet-4:
First Address: 121.37.10.112 /28
Last Address: 121.37.10.127 /28

## Slide 24: Fixed Length subnet masking – continued…
Since 4 subnets are required, we need 2 bits to identify each subnet. Thus the subnet mask now becomes (/28)..
Number of variable bits left = 32 -28 = 4 bits. Thus the total number of addresses in each subnet= 24= 16.
Address space divided into 4 equal sized subnets

## Slide 25
Fixed Length subnet masking – continued…

## Slide 26
Fixed Length subnet masking – continued…

## Slide 27
Fixed Length subnet masking – continued…

## Slide 28
Fixed Length subnet masking – continued…

## Slide 29: Problem – 2

## Slide 30: Problem#2
We have a big single network having IP Address 200.1.2.0.
We want to do subnetting and divide this network into 2 subnets.
Solution:
Clearly, the given network belongs to class C.
For creating two subnets and to represent their subnet IDs, we require 1 bit. So,
  We borrow one bit from the Host ID part.
  After borrowing one bit, Host ID part remains with only 7 bits.
  If borrowed bit = 0, then it represents the first subnet.
  If borrowed bit = 1, then it represents the second subnet

## Slide 31: Problem#2

## Slide 32: Problem#2
For 1st Subnet-
IP Address of the subnet = 200.1.2.0
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.00000000, 200.1.2.01111111] = [200.1.2.0, 200.1.2.127]
Direct Broadcast Address = 200.1.2.01111111 = 200.1.2.127
Limited Broadcast Address = 255.255.255.255
For 2nd Subnet-
IP Address of the subnet = 200.1.2.128
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.10000000, 200.1.2.11111111] = [200.1.2.128, 200.1.2.255]
Direct Broadcast Address = 200.1.2.11111111 = 200.1.2.255
Limited Broadcast Address = 255.255.255.255

## Slide 33: Problem - 3

## Slide 34: Problem - 3
We have a big single network having IP Address 200.1.2.0.
We want to do subnetting and divide this network into 4 subnets.
Clearly, the given network belongs to class C.
For creating four subnets and to represent their subnet IDs, we require 2 bits. So,
  We borrow two bits from the Host ID part.
  After borrowing two bits, Host ID part remains with only 6 bits.
  If borrowed bits = 00, then it represents the 1st subnet.
  If borrowed bits = 01, then it represents the 2nd subnet.
  If borrowed bits = 10, then it represents the 3rd subnet.
  If borrowed bits = 11, then it represents the 4th subnet.

## Slide 35: Problem#3

## Slide 36: Problem#3
For 1st Subnet-
IP Address of the subnet = 200.1.2.0
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.00000000, 200.1.2.00111111] = [200.1.2.0, 200.1.2.63]
Direct Broadcast Address = 200.1.2.00111111 = 200.1.2.63
Limited Broadcast Address = 255.255.255.255
For 2nd Subnet-
IP Address of the subnet = 200.1.2.64
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.01000000, 200.1.2.01111111] = [200.1.2.64, 200.1.2.127]
Direct Broadcast Address = 200.1.2.01111111 = 200.1.2.127
Limited Broadcast Address = 255.255.255.255

## Slide 37: Problem#3
For 3rd Subnet-
IP Address of the subnet = 200.1.2.128
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.10000000, 200.1.2.10111111] = [200.1.2.128, 200.1.2.191]
Direct Broadcast Address = 200.1.2.10111111 = 200.1.2.191
Limited Broadcast Address = 255.255.255.255
For 4th Subnet-
IP Address of the subnet = 200.1.2.192
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.11000000, 200.1.2.11111111] = [200.1.2.192, 200.1.2.255]
Direct Broadcast Address = 200.1.2.11111111 = 200.1.2.255
Limited Broadcast Address = 255.255.255.255